## Slide 1
One remote motor move (serial → CANopen → serial)
Master = HAT+ ESP32 (UC2_canopen_master). stepperid 1 (X) is routed to node 11, OD sub-index stepperid+1 = 2. A local axis skips steps 3–4 and 6–7.
Host (uc2rest)
ESP32 master
node 1 | DeviceRouter
Motor satellite X
node 11
1 /motor_act | stepperid 1 | position 1000 | speed 20000 | qid 5
2 RoutingTable: MOTOR 1 → REMOTE, node 11, subAxis 1
(LOCAL would start FastAccelStepper directly)
3 expedited SDO writes to 0x60B, each acknowledged on 0x58B:
0x2000:02 target | 0x2002:02 speed | [0x2006:02 accel]
0x2007:02 is_absolute | 0x200B:02 is_forever
4 SDO 0x2003:00 = 0x02 (bit n = start slot n, bit n+4 = stop slot n)
5 ack: {"steppers":[{"stepperid":1,"isDone":0}],"qid":5}
6 TPDO1 0x18B: position i32 | status (bit0 running = 1) | homing u8
on change (≥ 10 ms apart) and every 500 ms
7 TPDO1 0x18B: running = 0 → master sees the stop edge
8 {"steppers":[{"stepperid":1,"position":1000,"isDone":1}],"qid":5}
9 {"qid":5,"state":"done"} (QidRegistry, all axes of qid 5 done)
Feedback for steps 6–7 arrives only from nodes 10–13:
the master's RPDOs listen on fixed COB-IDs 0x18A–0x18D.
With uc2canopen (path B) the Pi sends 3–4 itself and reads 6–7 directly.

## Slide 2
UC2 control topologies
One CANopen master (node 1) per bus. Satellites are CANopen slaves. Node IDs shown are firmware defaults.
A | Standalone board v4
Host sends JSON over USB. v4 drives its own axes; CAN carries illumination and galvo.
Host: PC or Raspberry Pi
ImSwitch | uc2rest (Python) | WebSerial | any serial terminal
USB serial | JSON | 115200 8N1
Standalone board v4 (ESP32)
env UC2_canopen_standalone_v4_release | CANopen master, node 1
Motors A X Y Z
TMC2209 | local
Lasers 1–3
PWM | local
LED ring
local + CAN mirror
DeviceRouter: each device id is routed LOCAL or to a CAN node.
Laser id 4, LED array and galvo → CAN by default.
TWAI | TX GPIO32 / RX GPIO33
500 kbit/s | CAN_H solid / CAN_L dashed | 12 V on JST-XH 4
Illumination board
node 30 | LED + laser id 4
Galvo board
node 40
Extra CAN motors (stepperid ≥ 4) are not routed by this
firmware yet. Use the HAT+ topology (B) for CAN axes.
B | Raspberry Pi 5 + HAT+ (FRAME)
Two ways onto the same bus: via the ESP32 master (A) or directly via can0 (B).
Raspberry Pi 5
ImSwitch | uc2rest (path A) | uc2canopen (path B)
HAT+ v2 | J102 JST-XH 4 | 120 Ω jumper JP801
ESP32-WROOM-32E
env UC2_canopen_master
CANopen master, node 1
bus power GPIO4 | E-stop GPIO34
MCP2515 + SN65HVD230
Linux SocketCAN can0
12 MHz crystal | INT GPIO12
Pi GPIO23 cuts bus power
path A | JSON | 921600
UART GPIO14/15 or USB-C
path B | SPI0 CE0
INT GPIO12
TWAI TX17 / RX18
SDO / PDO direct
Motors A X Y Z
nodes 10–13
Laser board
node 20 | ch 0–3
LED / illum.
node 30
Galvo
node 40
GPIO / E-stop
node 60
PTZ keyboard
bridge | node 61
PS4 USB host
bridge | node 5
Bridges send their own SDOs to the satellites (extra SDO clients on the bus).
serial JSON
CAN / CANopen, 500 kbit/s
SPI
Terminate both physical ends of the bus with 120 Ω, nowhere else.

## Slide 3
HAT+ v2 (Rev D): who talks to what
Two CAN controllers share one bus: the ESP32 (CANopen master, node 1) and the Pi's own MCP2515 (can0). Designators from the v2 PCB.
Raspberry Pi 40-pin (J104)
pin | GPIO | function
8 | 10
GPIO14 TXD | GPIO15 RXD
UART to ESP32 (parallel to CP2102)
11 | 36
GPIO17 | GPIO16
RTS / DTR auto-program (JP901/902)
19 21 23 24
SPI0 MOSI MISO SCLK CE0
to MCP2515
32
GPIO12
MCP2515 interrupt
16
GPIO23
bus power off (high = off)
3 | 5
GPIO2 | GPIO3 (I2C-1)
to on-board I2C via JP101/102 (open)
The HAT also feeds the Pi 5.1 V / 5 A.
CP2102 (U701) | USB-C J103
USB serial to a PC / the Pi
ESP32-WROOM-32E (U101)
UART0 | JSON | 921600 Bd
GPIO17 → CAN TX
GPIO18 ← CAN RX
GPIO4 → bus power off
GPIO34 ← E-stop sense
I2C 21/22: INA226, TMP102
EN/IO0
MCP2515 (U901)
SPI CAN controller | 12 MHz (Y901)
Linux: mcp2515-can0 overlay → can0
SN65HVD230
U1101 | ESP32 side
TX17
RX18
SN65HVD230
U1001 | Pi side
CAN_H
CAN_L
J102 | JST-XH 4 | bus out
1 GND
2 +12 V (switched)
3 CAN_H
4 CAN_L
Bus power switch
12 V in J101 → J102 pin 2
off if ESP32 GPIO4 or Pi GPIO23 high,
or E-stop J501 opened
+12 V to satellites (JST-XH pin 2)
serial: /state_act {"power":0 or 1}